## Slide 1
WHAT?
Air sealing above-grade sill plates:
Can minimize air leakage from conditioned space
Provides a continuous air barrier where the wall meets the foundation
FLOOR FRAMING AIR SEALING SILL PLATES
Notes: Air sealing above-grade sill plates that are adjacent to conditioned space can minimize air leakage and helps provide a continuous air barrier where the wall meets the foundation.

## Slide 2
WHY?
For a home to perform efficiently, the walls, ceiling, and foundation must be connected to provide a continuous air barrier
Any seams where two different building components come together in the building shell represent a potential source of air leakage
The sill plate where the wall meets the concrete foundation is especially susceptible
Notes: For a home to perform efficiently, the walls, ceiling, and foundation must be connected to provide a continuous air barrier. Any seams where two different building components come together in the building shell represent a potential source of air leakage. The sill plate where the wall meets the concrete foundation is especially susceptible.

## Slide 3
HOW?
The sill plate-foundation wall juncture is sealed with a pliable closed-cell foam product
It is rolled out over the concrete along the foundation perimeter, where it conforms to any irregularities in the surface
The top of the sill plate is sealed to the rim joist with a bead of caulk, as are all joints in the sill plate
Notes: To air seal the junction between the sill plate and foundation, use a pliable closed-cell foam product that can be rolled out over the concrete along the foundation perimeter, where it conforms to any irregularities in the surface. All joints in the sill plate should be sealed with caulk, and the top of the sill plate should be sealed to the rim joist with a bead of caulk.